## Slide 1: DHCP, NAT, Mobile IP, Bluetooth, Ipsec, ATM
Clark Elliott
Clark Elliott
Notes on
Dynamic Host Configuration Protocol
Network Address Translation
Etc.
From Coulouris, Dolimore, Kindberg, and CDE

## Slide 2: Dynamic Host Configuration Protocol -- DHCP
Clark Elliott
Large organizations like DePaul have leases on large numbers of real IP addresses.
But faculty, administration, and lab machines come and go. One IP address for each student is also a big burden.
Deciding who is bound to which IP address is a giant administrative nightmare: setting up each user’s machine (or multiple machines) is a giant time sink. Each machine has to be configured before it can use the network.

## Slide 3
Clark Elliott
Much more efficient to allocate IP address only when they are needed, on an ad hoc basis, without administration, from a pool of valid, real, IP addresses.
When a user boots their machine, the DHCP client broadcasts a query to the DHCP server, which returns a valid IP address, a lease length, subnet mask, and default gateway.
The crucial item: A VALID REAL IP ADDRESS

## Slide 4: Three methods of DHCP allocation
Clark Elliott
Dynamic: just give a client whatever is available from the pool at the time of the request. Typical use. Easy to implement. No administration.
Automatic: Like dynamic, but keep track of what you’ve allocated, and always give that IP address to the client.
Static: keep the MAC addresses of the clients in a table. When that MAC makes a request, assign them the associated IP address in the table. Lose many of the efficiencies, but don’t have to configure clients.

## Slide 5: Efficiency
Clark Elliott
DHCP thus allows an organization to support many more computers than it has IP addresses, depending on who needs an IP address at any given moment.
The biggest savings is in not having to administer the system. New machines and old machines alike configure themselves.

## Slide 6: NAT is not DHCP
Clark Elliott
Network Address Translation is something completely different.
It also allows many more computers to use the internet than there are real IP addresses.
NAT assigns users “FAKE” (local) IP addresses that cannot be used directly on the internet.
NAT addresses work fine on local networks.
NAT addresses are not unique. Many thousands (millions?) of users will be using the same NAT IP address at any given moment.

## Slide 7
Clark Elliott
A typical NAT installation is a home or office that has many computers, but little need to support servers. Internet use is primarily as clients.
A NAT-enabled router is required, through which the local network operates.

## Slide 8: Network Address Translation
Copyright 2008 Clark Elliott
Used in millions (?) of homes / offices
192.168.x.x is reserved for “home” domains, these are fake IP address primarily for internal IP hosts that operate as clients to internet.

## Slide 9: Network Address Translation
Copyright 2008 Clark Elliott

## Slide 10: How NAT works…
Copyright 2008 Clark Elliott
Local host (lhost) sends request packet to internet via the NAT-enabled router
Router saves the request IP/port in table
Replaces the IP/Port with router’s IP address and a virtual port that indexes the entry in the table.
Sends to destination server with router IP/virtual port

## Slide 11
Copyright 2008 Clark Elliott
When the server replies, it uses the router IP/virtual port
The router receives the reply, uses the (virtual) port for table lookup, replaces router IP/virtual port with the local IP and port of lhost.
Sends to ethernet
Original sender retrieves from the local network.
Keep entries for a while, then discard

## Slide 12: Servers on NAT
Copyright 2008 Clark Elliott
With many ISPs the router IP changes, so have to have a forwarding site to translate domain name, and wait for propagation.
External clients use IP of router (or domain name pointing to it), and a specific port.
Router forwards all incoming traffic for that port to the lhost at some manually assigned port.
Lhost servers cannot use relative DHCP

## Slide 13: Servers on your laptop
Copyright 2008 Clark Elliott
When you take your laptop to a new location it discovers the local subnet and gets a local IP address from DHCP.
Your laptop can now act as a client.
Legacy service conversations with servers on your laptop can no longer find you.
Address forwarding software can work around this, though with some drawbacks.

## Slide 14: Mobile IP
If server push is required, or others are using local resources that are mobile, then DHCP will not work
IP address are subnet-based, for routing purposes, geographically fixed.
Mobile IP uses home agent (HA) and foreign agent (FA).
HA acts as a proxy to reroute all packets through a tunnel.
Mobile-IP-enabled senders can communicate directly thereafter

## Slide 15: Your laptop
Copyright 2008 Clark Elliott
When you take your laptop to a new location it discovers the local subnet and gets a local IP address from DHCP.
Your laptop can now act as a client.
Legacy service conversations with servers on your laptop can no longer find you.
Address forwarding software can work around this but either low efficiency (every packet is forwarded) or both sides have to know to dynamically update the service address after initial handshaking.

## Slide 16: Home agents and Foreign Agents
Copyright 2008 Clark Elliott
Run at home host, and foreign host
HA must have up-to-date knowledge of the IP location of mobile host (mhost).
HA tells local routers to get rid of cached records of mhost.
HA uses ARP (Address Request Protocol) to accept packets as a proxy for mhost.
Mhost works with FA to inform HA of where it is.
HA forwards packets wrapped in Mobile-IP packets.
FA passes to Mhost.
If sender is Mobile-IP enabled, can now communicate directly, otherwise repeat.
Servers can now be mobile.

## Slide 17: Figure 3.20 The MobileIP routing mechanism
Sender
Home
Mobile host MH
Foreign agent FA
Internet
agent
First IP packet
addressed to MH
Address of FA
returned to sender
First IP packet
tunnelled to FA
Subsequent IP packets
tunnelled to FA

## Slide 18: Not best solution
Copyright 2008 Clark Elliott
Requires HA.
Setup time
Requires clients to be Mobile-IP or have to route ALL packets twice.
Mobile phones are first-class citizens as they move from cell to cell.

## Slide 19: Mobile agents
Processes, code libraries, and state that move from one location on a network to another to perform work on a remote location’s behalf.
Interact with local resources, such as databases, other processes, and even users.
Local invocations are cheaper than remote ones so may lead to efficiency.
Different programming design
Security and negotiation are complex because always two different stakeholders, host / agent

## Slide 20: Mobile agents
One generally unexplored area is using the idle resources of a nework
Security problems can work both ways: both to the host, but also to the agent.
Not hugely popular. Note that web crawlers “look” like agents, but are simply a series of local requests to various servers.

## Slide 21: Mobile devices
Wave of the future. Miniaturization of CPUs, lower power requirements, improved battery technology, wireless technology
WiFi – term does not mean anything, just catchy
In general DHCP and discovery of local resources is enough as a collection of clients

## Slide 22: IPv6
Copyright 2008 Clark Elliott
128 bit addressing, or 1000 IP addresses per square meter of earth’s surface
Geographic and organizational semantics in addresses
Flow labels for QoS improvements
Security headers – but note that destinations are not encrypted (?), authentication for RIP
Slow migration, but 1 billion Devices in China and India by 2014, plus mobile IP needs.

## Slide 23: IPsec (“IP security”)
Copyright 2008 Clark Elliott
Operates at a lower level than TSL, SSL, SSH, so applicable to wide range of applications including basic TCP and UDP without requiring rewrite apps. Provides:
  Encrypting traffic (so it cannot be read by parties other than those for whom it is intended)
  Integrity validation (ensuring traffic has not been modified along its path)
  Authenticating the peers (ensuring that traffic is from a trusted party)
  Anti-replay (protecting against replay of the secure session).
Uses IKE internet key exchange
Mandated in IPv6, but forced onto IPv4 by need.

## Slide 24: VPNs
Copyright 2008 Clark Elliott
Virtual Private Networks
Based on IPsec
Typical: home ISP user exchanges keys with firewall, and can then access intranet
Can also connect two intranets

## Slide 25: Bluetooth IEEE 802.15, 2002
Copyright 2008 Clark Elliott
Developed by Ericsson.
Voice and data
$5 per device
Low battery consumption – several hours even with earpiece battery. Wake up and listen for a paging call, so long latency to establish contact.
Adaptable power transmission from 1 Mwatt (10 meters) to 100Mwatt (100 meters)
Switches 1600 times / second between 79 sub-bands of 2.4 GHz public frequency for reduced interference

## Slide 26: Master / slave
Copyright 2008 Clark Elliott
Pairs operate as master / slave, with master allocating communication slots
Piconet – up to 7 slaves one master and up to 255 parked (dormant) slaves in low power mode waiting for a wakeup signal.
Scatternet – linked piconets.
Most devices can be master or slave.
All devices have 48-bit GUIDs, but slaves assigned 1-7 to save space.

## Slide 27: Bluetooth…
Copyright 2008 Clark Elliott
Designed for QoS required of audio.
Synchronous and async transfer.
Up to 1 Mbps
Includes specifications for app-level protocols to encourage interoperation of manufactured devices.
Association of new / parked devices is slow, up to 10 seconds – so not for e.g., toll road pickup of vehicles.
Version 2.0: 3 Mbps (cd quailty audio), larger piconets, faster association is in the works.

## Slide 28: Figure 3.27 ATM cell layout

## Slide 29: ATM – asynchronous transfer mode
Copyright 2008 Clark Elliott
Fast packet switching w/ suitable QoS for multimedia transmission
Avoids flow control and error checking
Fixed-length units of data (cells) 53 bytes
Establishes a connection first, guarantees bandwidth and latency. Frame relay does not store cell/frame.
High-speed switching, low latency
Similar speed to LANs.
High QoS and speeds of 600Mbps for multimedia will be available for internet.
Pure ATM up to 1 Gbps.
Slow to adopt because of expense compared to e.g., 1000Mbps ethernets.

## Slide 30: Have to address…
No global clock
Communication is via messages (without clock!)
Delays, and high failure
Vulnerable to attacks on message system
Remote administration problems
Massive scale-up problems
Classic problems like the server-binding problem

## Slide 31: Falacies
Copyright 2008 Clark Elliott
Eight fallacies of distributed computing: 1. The network is reliable. 2. Latency is zero. 3. Bandwidth is infinite. 4. The network is secure. 5. Topology doesn't change. 6. There is one administrator. 7. Transport cost is zero. 8. The network is homogeneous.

## Slide 32: Figure 2.1 Software and hardware service layers in distributed systems

## Slide 33: Layers
Hardware, microcode, bit level binary code and assembly. OpSys privlidged and user operations. [Virtual OpSys], shell wrapper, [application VM], Middleware, application
Middleware provides homogenous interface for application development. May handle, e.g., message passing, buffering, reliability, security.

## Slide 34: Middleware
RPC, RMI, DCE, sockets, CORBA, .net
Always a compromise: ease of use vs. reliability, efficiency, and maintainability of the middleware.
  Example. Very large mail file. Application probably needs to keep a local copy to resend if there are major network problems, and not just rely on TCP.

## Slide 35: Peer-to-peer
Claim is made that client/server does not scale well, but, of course, this is nonsense.
It does not scale automatically, but instead requires the expansion of network, server machines, etc.
Peer to peer e.g., can take advantage of massive wasted computer power sitting on desktops. Napster, Kazza, Gnutella, BitTorrent

## Slide 36: Peer-to-peer
Forces nodes to contribute.
Same functional characteristics at most, if not all, nodes
No central authority or failure point.
Can provide anonymity
Balances workload across nodes
Large address space via GUIDs
Best for static data because secure hash discourages malicious nodes.

## Slide 37: Figure 2.3 A distributed application based on peer processes

## Slide 38: Services
Logically decoupled from the endpoint (ip address / port) of any particular server, but instead clients subscribe to a service that might be provided by many servers.
Might have redundancy (replication), or specialization (partitioning) so that multiple servers participated for single client.

## Slide 39: Figure 2.4 A service provided by multiple servers

## Slide 40: Proxy servers
Extra server level that acts as a filter for requests
Caching for efficiency, firewall for protection, route to redundant servers for availability and ease of maintenance, mobile IP routing.
Typical: caching of popular web pages

## Slide 41: Figure 2.5 Web proxy server

## Slide 42: Mobile Code
Code moves from one location to another before or during execution
Strong mobility – running processes moved while in progress
Weak mobility – always started from the beginning after moving. Java applets.
Code may communicate with server

## Slide 43: Figure 2.6 Web applets

## Slide 44: Mobile agents
Processes, code libraries, and state that move from one location on a network to another to perform work on a remote location’s behalf.
Interact with local resources, such as databases, other processes, and even users.
Local invocations are cheaper than remote ones so may lead to efficiency.
Different programming design
Security and negotiation are complex because always two different stakeholders, host / agent

## Slide 45: Mobile agents
Security problems can work both ways: both to the host, but also to the agent.
Not hugely popular, but this does not mean they are not the best solution! The old way is not always the best way.
Note: these are not web crawlers which “look” like agents, but are simply a series of recursive local requests to various servers.

## Slide 46: A hypothetical case
Acme Agents provides optimization software for large proprietary construction company databases.
Ng Construction Company doesn’t want to leak anything about its customer base, business models, or contracts.
Ng is leery about running software that has a real-time connection over the internet through which their data passes.

## Slide 47: Acme Agent’s concerns
Acme Agents uses a database of its own tweaked for construction company DBs.
They are reluctant to send their software to Ng and possibly expose their intelligent optimization data, putting them out of business if it leaks.
It is expensive to send a person to the various construction company sites.

## Slide 48: General constraints
This is a large database, with e.g., many image PDFs of contracts, and construction photos.
It is computationally expensive to ship the data over network lines.
Optimization problems occur at times of high load, and DB queries are much better done locally.

## Slide 49: A hypothetical agent solution
Acme ships an optimization agent to Ng, which agent maintains its own internal state.
Protocols are set up for the two stakeholders to protect their states. Ng and Acme and work through a dual-direction “firewall.”

## Slide 50
The database is queried and stressed locally by the agent, using the intelligent software and knowledge contained in the agent, such that information is gained, tests are run, solutions tried, but all working with the local company Ng to not disrupt business use.

## Slide 51
Acme learns more about the problems that can occur in large construction company DBs, along with solutions that (a) work and (b) that don’t work. Acme stores this knowledge in the state of the agent.
Design/optimization problems (only), stripped of client business information is shipped back to Acme for review during the optimizing process as needed for human intervention

## Slide 52: Agent returns home, the off to work again.
After making/recommending optimizations to Ng’s database, the Acme agent is shipped back to Acme, along with its new internal state.
When Lee construction company next hires Acme to optimize its database, the knowledge about optimization of construction databases is used, but none of Ng’s business model, or its customer base is exposed.

## Slide 53: Benefits
Lee construction gets better, faster, cheaper optimization.
So does Ng the next quarter when Acme returns next quarter with the knowledge from Lee’s optimization event.
Acme manages optimization knowledge, and Ng and Lee manage construction knowledge.

## Slide 54
Neither Ng nor Lee has their business data exposed.
No one else can snoop on business data traversing the internet.
Realistic control of stressing a database locally.
Part of the internal state is the relationships the agent maintains to other entities—in this case Ng and Lee, which persists.

## Slide 55
This is a variation of shipping the executable code to the site of big data.
The critical element is that agents maintain their own (often protected) internal state.

## Slide 56: Network computers
Manage files and other critical resources in a central location, correctly, under opsys control. Make transparent to users.
Very thin client
Local disk is primarily for caching
Remote desktops are related, X-11 runs local display server on the user machine
Lucent’s plan 9: http://www.ecf.toronto.edu/plan9/plan9faq.html

## Slide 57: Mobile devices
Wave of the future. Miniaturization of CPUs, lower power requirements, improved battery technology, wireless technology
WiFi – term does not mean anything, just catchy
In general DHCP and discovery of local resources is enough as a collection of clients

## Slide 58: Mobile IP
If server push is required, or others are using local resources that are mobile, then DHCP will not work
IP address are subnet-based, for routing purposes, geographically fixed.
Mobile IP uses home agent (HA) and foreign agent (FA).
HA acts as a proxy to reroute all packets through a tunnel.
Mobile-IP-enabled senders can communicate directly thereafter

## Slide 59: Discover card goofiness
Password for discover account was sent to me as clear text in email after a problem, and not at my request.
Exposed to internet attack, exposed to attack on my unix machine, exposed to mail process attack.
Was original password I typed in a month earlier, which means what…?!!
Argued for twenty minutes with the “top security guy” who was an idiot.

## Slide 60: AT&T Security Evil / Morons
To: [...]@yahoo.com
Subject: AT&T Password Reset
Dear Valued Customer,
  Cellular Data Number is 858-xxx-nnnn
  Your password is [xxxxxxxx]. Please use it when logging into your account via Settings on your iPad.
Thank You,
AT&T

## Slide 61: Cryptographic Salt
Random bit-string added to password before producing the encrypted version of the password. Stored on the server.
Increases the randomness and the length of the password string.

## Slide 62: Communication channels
Latency – time between the start of a message send, and the start of the receipt at the other end. (Time to send an empty packet.) For acknowledgments requires roughly 2x latency value.
Affected by distance, reliability of network (resends), layers of software, load on network and OpSys, security overhead (e.g., encrypting messages), proxies, superservers and service startup, load-balancing servers.

## Slide 63
Satellites have high throughput, but high latency values – so bad for interactive editing, but good for downloads

## Slide 64: Bandwidth
Maximum number of bits that can be transmitted over the network in a given period of time.
Affected by overhead bits, errors, sharing loads with all processes.
May vary greatly. Routing changes and loads are all dynamic.
Measured as an average

## Slide 65: Jitter
Variation in time to deliver individual messages
Difference between maximum and minimum times.
Very important to audio streams, and streams that combine video and audio.

## Slide 66: Clocks
Individual computers each have their own clocks.
Typically billions of cycles different.
Local processes read local clocks.
Perfect external reference clock – even if it existed, the time cannot be read in except through millions of instructions.
So – time stamps are not very meaningful in a distributed system. (Remember the cached data?)

## Slide 67
Can use GPS attached to a computer, but not all boxes have radio access – but sending on local network is subject to message delay. Only good for mSec anyway (when a million instructions might be executed).
Network time protocol. Other schemes to set clocks approximately.

## Slide 68: Bits & Bytes
11/2/2016
Copyright Mark Goetsch
68
Transmission quantity is measured in 10^n so that 64K is 64 x 1000 or 64,000.
Computer quantity is measured in 2^n so that 64K is 64 X 1024 or 65,536.
This is a difference of 2.34%. Close enough for government work??
Here is a twister -> Remember the calculation for Transmission Time?
Transmission Time = RTT + (Transfer Size / Bandwidth)
We have a 100 ms RTT, a 64K sized file, and a 64K single channel.
TT = .1 s+ (64 * 1024 * 8) bps / (64 * 1000) bps
TT = 8.292 s
File size and storage is measured in terms of bytes but transmission is measured in terms of bits (i.e. don’t’ forget to multiply/divide by 8).
Notes: 68

## Slide 69: Binary Bytes vs. Decimal Bytes
Copyright 2008 Clark Elliott
Network, 1K = 1,000, 1M = 1,000,000
Computer 1K = 1024, 1M = 1,048,576
  Except disk drives use powers of ten to artificially inflate the size of the drive.
  1 Terabyte disk drive = 931 GB
So how long does it take to send the payload of 1 GB of data over a “1 GB” network line?
http://www.codinghorror.com/blog/2007/09/gigabyte-decimal-vs-binary.html

## Slide 70: It’s not rocket science – or is it?
Copyright 2008 Clark Elliott
The power of ten / powers of two problem causes communication problems between CS people and IT people
IT managers MUST understand this issue
“NASA lost a $125 million Mars orbiter because a Lockheed Martin engineering team used English units of measurement while the agency's team used the more conventional metric system for a key spacecraft operation, according to a review finding released Thursday.” (http://www.cnn.com/TECH/space/9909/30/mars.metric.02/ )

## Slide 71: Calculating RTT, Throughput, and Transfer Time
11/2/2016
Copyright Mark Goetsch
71
RTT is 2 X Latency and is the round trip time delay
Transfer Time = RTT + (Transfer Size/Bandwidth)
Throughput = Transfer Size/Transfer Time
Example: User wants to fetch a 1MB file across a 1 Gbps network with a 50 ms latency.
RTT = 2 X Latency = 100 ms
Transfer Time = .1 sec + (8 X 1,048,576)/1,000,000,000
= .1 sec + .008 sec
= 108 ms
Throughput = (8 X 1,048,576)/.108 sec = 77,393,816
= 77Mbps and not 1Gbps.
Notes: 71

## Slide 72: Switching schemes
Copyright 2008 Clark Elliott
Broadcast – ethernet, WiFi. No routing
Circuit switching – throw switches in line to prepare a circuit. POTS (plain old telephone system), train tracks.
Packet switching – processing and storage of computers allows free real-time routing
Frame relay – inspect first few bits, then pass on frame without storing or inspection. ATM uses this. Very fast, parallel, establish virtual circuit first.

## Slide 73: Protocols
Copyright 2008 Clark Elliott
Set of rules and formats
Specification of sequence of messages to exchange
Specification of the data format

## Slide 74: OSI Protocol Stack Implemented
April 30, 2008
Copyright Mark Goetsch
74
Notes: 74

## Slide 75: Layers  object code
Copyright 2008 Clark Elliott
Each layer makes library calls to the level below which get included in the object code, or as SVC to operating system.
Fully compiled code might have all layers compiled into executable, with entry point into running OpSys procs or kernal code.
Each layer “hides” more complex code below.

## Slide 76: Layers of detail – one line of app code = ~1500 lines of “real” code.
Copyright 2008 Clark Elliott
Java App: “open a socket”
.TCP / IP: bind, connect, listen…
..Allocate application buffers
…TCP: handshaking with other host, ports…
…. Transport: break messages into units, route
….. Allocate OpSys buffers
…….[etc.]
………translate to MAC ethernet…

## Slide 77: Figure 3.2 Conceptual layering of protocol software
Layer n
Layer 2
Layer 1
Message sent
Message received
Communication
medium
Sender
Recipient

## Slide 78: Figure 3.4 Protocol layers in the ISO Open Systems Interconnection (OSI) model

## Slide 79: Figure 3.3 Encapsulation as it is applied in layered protocols

## Slide 80: Figure 3.13 Encapsulation in a message transmitted via TCP over an Ethernet
Application message
TCP header
IP header
Ethernet header
Ethernet frame
port
TCP
IP

## Slide 81: Figure 3.14 The programmer's conceptual view of a TCP/IP Internet

## Slide 82: IANA Port Assignments
April 30, 2008
Copyright Mark Goetsch
82
Updated this month http://www.iana.org/assignments/port-numbers
Port # | Service | Protocol
21 | FTP | TCP/UDP/SCTP
23 | Telnet | TCP/UDP
25 | SMTP | TCP/UDP
80 | HTTP | TCP/UDP/SCTP
88 | Kerberos | TCP/UDP
118 | SQL Server | TCP/UDP
443 | HTTPS | TCP/UDP/SCTP
Notes: 82

## Slide 83: Migration to IPv6
Copyright 2008 Clark Elliott
Address space has run out under IPv4
A new standard IPv6 allows for many more addresses, and also includes improvements for security, multimedia QOS, and routing efficiency.
Replaces IPv4 and is not compatible.
Tunneling allows for graceful adoption.

## Slide 84: IPv6
Copyright 2008 Clark Elliott
128 bit addressing, or 1000 IP addresses per square meter of earth’s surface
Geographic and organizational semantics in addresses
Flow labels for QoS improvements
Security headers – but note that destinations are not encrypted (?), authentication for RIP
Slow migration, but 1 billion Devices in China and India by 2014, plus mobile IP needs.

## Slide 85: Figure 3.11 Tunnelling for IPv6 migration
A
B
IPv6
IPv6
IPv6 encapsulated in IPv4 packets
Encapsulators
IPv4 network

## Slide 86: Conversion IP / local network address
Copyright 2008 Clark Elliott
Different local networks have different addressing schemes.
Ethernet is common, and has 48-bit addresses – ARP (address resolution protocol) is used to translate to/from IP.
Sender: broadcast IP address query.
Receiver: send back MAC address of NIC.
Sender: place pair in table, then send packet using MAC address.
Once all pairs are discovered, no query
Beyond local net, get MAC of gateway & send

## Slide 87: TCP & UDP
Copyright 2008 Clark Elliott
Transport protocols, process-to-process communication msgs, uses ports for this.
Processes acquire ports from the operating system through system calls.

## Slide 88: Universal Datagram Protocol - UDP
Copyright 2008 Clark Elliott
“IP up one level”
Source and dest ports for addressing
Length. Checksum optionally used by receiving host.
Cheap, fast.
No guarantees of delivery, or order of arrival.

## Slide 89: Trasmission Control Protocol - TCP
Copyright 2008 Clark Elliott
Reliable transmission of streams
Connection-oriented.
Guaranteed delivery in guaranteed order
IP does not know about it. End-to-end.

## Slide 90: TCP features
Copyright 2008 Clark Elliott
Guaranteed sequence – requires “infinite” buffer – wait for first packet to arrive
Flow control – windows, maximum delay before send, configurable, etc. so that receiver or network is not overwhelmed, and user does not have to wait too long.
Auto retransmission of packets as needed
Buffering as needed for flow control and ordering.

## Slide 91: TCP Protocol
April 30, 2008
Copyright Mark Goetsch
91
Connection-Oriented
The data is presented as a stream of data rather than a set of packets.
Reliable
Every piece of data will arrive.
Duplex
You can send information both ways at the same time, through the same connection.
Byte-Oriented
Data packets are delivered in the correct order.
How does this happen?
Notes: 91

## Slide 92: The Inner Workings of TCP
April 30, 2008
Copyright Mark Goetsch
92
Each TCP connection provides a buffer that will hold the data until it has been verified that it has arrived.
The buffer also is used to order the packets in the correct sequence.
Every packet that is sent requires an “Ack” from the receiver so that it knows that it has arrived.
A CRC field is added and checked by the receiver to see that the data was not corrupted.
Each connection is a 4-tuple consisting of the port numbers for both the client and server, and the IP addresses as well.
Which has quite a bit of overhead!
Notes: 92

## Slide 93: Ethernet
Copyright 2008 Clark Elliott
Cheap, reliable, local area network
Long time defacto standard at 10Mbps
100 Mbps is cheap, and 1000 Mbps available.
Broadcast of all packets
NICs listen to all traffic and normally ignore all that does match, pass those that do up the protocol stack.
Separate send and receive – don’t start send if other is.
Collisions can occur resulting in resends, and ultimately thrashing if overloaded. Longer cable / more collisions.
Use of switches/software, reduces collisions & helps guarantee latency and delivery for QoS. Not obsolete yet

## Slide 94: Ethernet
Copyright 2008 Clark Elliott
Uses CSMA/CD:
Sense if the line is free
Every computer has full-time access – Multiple Access
Detect collisions and resend after a random delay.
Medium Access Control (MAC) is protocol, hence MAC addresses are used in hrdwre

## Slide 95: Slot reservation extension to Ethernet
Copyright 2008 Clark Elliott
Collision avoidance augmentation via CSMA/CA; reserves transmission slots.
Short negotiation packets (Request to send, RTS; clear to send, CTS) are sent first between sender and receiver, with duration. Others wait until slot has passed.
Fewer collisions with short packets.
Improves wireless reliability and QoS.

## Slide 96
Clark Elliott
Note have not added CDK chapter 4 or 5 yet.